## Slide 1
Sesame – GenX comparison
Ruaridh Macdonald, Amanda Farnsworth
Version: 8th August, 2023

## Slide 2
Comparison Overview
We built a simplified model of ISO-NE which could be modelled by both Sesame and GenX, given the features and resources which can be modelled in both
Created two version of the GenX model:
  Used the full fusion model developed by the Grid Team
  Used a simplified representation closer to a fission power plant
Ran a quite of tests using both Sesame and GenX to compare:
  The total system cost: investment costs, fixed O&M, variable O&M, and fuel costs
  Installed capacity of each generator
  Capacity factor of each generator
Both models were fully linearized, removing ramping constraints, minimum powers, etc.

## Slide 3
Model Details
Resource | Capital Cost ($/kWe) | Fixed OM Cost ($/MWe/yr) | Variable OM Cost ($/MWh-e) | Fuel Cost ($/MMBtu)
Natural Gas CombCycle | 971 | 24,000 | 1.62 | 7.25
Nat Gas CombCycle + CCS | 1,658 | 40,000 | 3.32 | 8.20
Utility-scale Solar PV | 632 | 13,000 | 0 | 
Onshore Wind | 924 | 23,000 | 0 | 
4hr Li-ion | 2,314 | 71,000 | 0 | 
Fixed Offshore Wind | 250 | 6,395 | 0 | 
Fusion | 8,500 | 84,738 | 2.0 | 0
Generation and storage resources allowed in each zone
Resource | Utility-scale Solar PV | Onshore Wind
Maximum installed capacity (GWe) | 22 | 10
Maximum allowed installed capacity for certain resources, across all ISO-NE
QC
ISO-NE
Demand metric (MWe) | Mean | Median | Max | Min
ISO-NE | 21719 | 21867 | 42825 | 9912
Descriptions of electricity demand in each model zone over the 20 scenarios (MWe)

## Slide 4
Results: Summary
Model | Total Annual Cost ($ / year) | Installed Fusion Capacity
Sesame | 12,747,491,498 | 6,327
GenX – simple fusion | 16,927,890,588 | 11,059
GenX – full fusion | 17,367,417,823 | 10,403
Sesame @ 11GWe fusion | 13,508,535,766 | 11,059
Total system cost comparison
Without limits on onshore wind and solar PV capacity, both models showed no installed fusion at any emission limits
With caps on solar PV and onshore wind:
  Sesame showed ~50% fewer fusion power plants, and lower capacity factor
  More offshore wind capacity and Li-ion battery capacity displaces fusion
To compare further, we forced Sesame to install the same amount of fusion power plants

## Slide 5
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 0. | 0%
Nat Gas CombCycle + CCS | 12,127 | 13%
Utility-scale Solar PV | 22,000 | 
Onshore Wind | 10,000 | 
4hr Li-ion | 17,877 | n/a
Fixed Offshore Wind | 9,090 | 
Fusion | 11,059 | 85%
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 1,664 | 1%
Nat Gas CombCycle + CCS | 9,596 | 15%
Utility-scale Solar PV | 22,000 | 18%
Onshore Wind | 10,000 | 35%
4hr Li-ion | 16,221 | n/a
Fixed Offshore Wind | 7,458 | 49%
Fusion | 11,059 | 85%
Results
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 0. | 0%
Nat Gas CombCycle + CCS | 8,849 | 18%
Utility-scale Solar PV | 22,000 | 
Onshore Wind | 10,000 | 
4hr Li-ion | 74,546 | n/a
Fixed Offshore Wind |  | 
Fusion | 6,327 | 77%
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 1,196 | 0%
Nat Gas CombCycle + CCS | 10,357 | 15%
Utility-scale Solar PV | 22,000 | 18%
Onshore Wind | 10,000 | 35%
4hr Li-ion | 16,511 | n/a
Fixed Offshore Wind | 9,054 | 49%
Fusion | 10,403 | 82%
GenX results with full fusion plant model
Sesame results with simplified fusion plant model
Sesame results with simplified fusion plant model @ 11GWe Fusion
GenX results with simplified fusion plant model

## Slide 7
Results
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 0. | 0%
Nat Gas CombCycle + CCS | 8,849 | 18%
Utility-scale Solar PV | 22,000 | 
Onshore Wind | 10,000 | 
4hr Li-ion | 74,546 | n/a
Fixed Offshore Wind |  | 
Fusion | 6,327 | 77%
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 1,196 | 0%
Nat Gas CombCycle + CCS | 10,357 | 15%
Utility-scale Solar PV | 22,000 | 18%
Onshore Wind | 10,000 | 35%
4hr Li-ion | 16,511 | n/a
Fixed Offshore Wind | 9,054 | 49%
Fusion | 10,403 | 82%
GenX results with full fusion plant model
Sesame results with simplified fusion plant model
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 0. | 0%
Nat Gas CombCycle + CCS | 12,127 | 13%
Utility-scale Solar PV | 22,000 | 
Onshore Wind | 10,000 | 
4hr Li-ion | 17,877 | n/a
Fixed Offshore Wind | 9,090 | 
Fusion | 11,059 | 85%
Sesame results with simplified fusion plant model
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 1,664 | 1%
Nat Gas CombCycle + CCS | 9,596 | 15%
Utility-scale Solar PV | 22,000 | 18%
Onshore Wind | 10,000 | 35%
4hr Li-ion | 16,221 | n/a
Fixed Offshore Wind | 7,458 | 49%
Fusion | 11,059 | 85%
GenX results with simplified fusion plant model

## Slide 8
Results
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 0. | 0%
Nat Gas CombCycle + CCS | 8,849 | 18%
Utility-scale Solar PV | 22,000 | 
Onshore Wind | 10,000 | 
4hr Li-ion | 74,546 | n/a
Fixed Offshore Wind | 19,297 | 
Fusion | 6,327 | 77%
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 1,196 | 0%
Nat Gas CombCycle + CCS | 10,357 | 15%
Utility-scale Solar PV | 22,000 | 18%
Onshore Wind | 10,000 | 35%
4hr Li-ion | 16,511 | n/a
Fixed Offshore Wind | 9,054 | 49%
Fusion | 10,403 | 82%
GenX results with full fusion plant model
Sesame results with simplified fusion plant model
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 0. | 0%
Nat Gas CombCycle + CCS | 8,658 | 13%
Utility-scale Solar PV | 22,000 | 
Onshore Wind | 10,000 | 
4hr Li-ion | 43,857 | n/a
Fixed Offshore Wind | 10,369 | 
Fusion | 11,059 | 85%
Sesame results with simplified fusion plant model
Resource | Capacity (MWe) | Capacity Factor
Natural Gas CombCycle | 1,664 | 1%
Nat Gas CombCycle + CCS | 9,596 | 15%
Utility-scale Solar PV | 22,000 | 18%
Onshore Wind | 10,000 | 35%
4hr Li-ion | 16,221 | n/a
Fixed Offshore Wind | 7,458 | 49%
Fusion | 11,059 | 85%
GenX results with simplified fusion plant model