## Slide 1
Model Details: Summary
Resource | Discount Rate (%) | Lifetime | Capital Cost ($/kWe) | Annual Investment Cost ($/MWe/yr) | Annual Investment Cost w/ locational adjustment ($/MWe/yr) | Fixed OM Cost ($/MWe/yr) | Variable OM Cost ($/MWh-e) | Heat Rate (MMBtu/MWhe) | Fuel Cost ($/MMBtu) | Mean fuel cost ($/MWh-e) | Total Variable Cost ($/MWh-e)
Natural Gas CombCycle | 6 | 30 | 971 | 70,542 | 82,064 | 24,000 | 1.62 | 6.15 | 7.25 | 44.67 | 46.29
Nat Gas CombCycle + CCS | 6 | 30 | 1,658 | 120,452 | 125,471 | 40,000 | 3.32 | 6.85 | 8.20 | 49.68 | 53.00
Utility-scale Solar PV | 6 | 30 | 632 | 45,914 | 47,521 | 13,000 | 0 |  |  | 0 | 0
Commercial Solar PV | 6 | 30 | 861 | 62,550 | 64,740 | 10,000 | 0 |  |  | 0 | 0
Residential Solar PV | 6 | 30 | 1,119 | 81,294 | 84,139 | 14,000 | 0 |  |  | 0 | 0
Onshore Wind | 6 | 30 | 924 | 67,128 | 69,365 | 23,000 | 0 |  |  | 0 | 0
Fixed Offshore Wind | 6 | 30 | 2,314 | 168,110 | 196,268 | 71,000 | 0 |  |  | 0 | 0
Floating Offshore Wind | 6 | 30 | 3,743 | 271,925 | 317,472 | 61,000 | 0 |  |  | 0 | 0
Li-ion Battery | 6 | 30 | 250 | 18,162 | 18,707 | 6,395 | 0 |  |  | 0 | 0
Pumped Hydro Storage |  |  | n/a | n/a | n/a | 18,700 | 0 |  |  | 0 | 0
Run-of-River Hydro |  |  | n/a | n/a | n/a | 47,000 | 0 |  |  | 0 | 0
Reservoir Hydro |  |  | n/a | n/a | n/a | 18,700 | 0 |  |  | 0 | 0
Fusion | 6 | 40 | 8,500 | 564,923 | 631,584 | 84,738 | 2.0 | 10.54 | 0 | 9.34 | 11.34
Fusion fuel cost is from vacuum vessel degradation.
This value assumes 100% capacity factor

## Slide 2
Model Details: Summary
Resource | Discount Rate (%) | Lifetime | Capital Cost ($/kWe) | Annual Investment Cost ($/MWe/yr) | Annual Investment Cost w/ locational adjustment ($/MWe/yr) | Fixed OM Cost ($/MWe/yr) | Emissions Intensity | Heat Rate (MMBtu/MWhe) | Fuel Cost ($/MMBtu) | Mean fuel cost ($/MWh-e) | Total Variable Cost ($/MWh-e)
Natural Gas CombCycle | 6 | 30 | 971 | 70,542 | 82,064 | 24,000 | 0.05306 | 6.15 | 7.25 | 44.67 | 46.29
Nat Gas CombCycle + CCS | 6 | 30 | 1,658 | 120,452 | 125,471 | 40,000 | 0.005306 | 6.85 | 8.20 | 49.68 | 53.00
Utility-scale Solar PV | 6 | 30 | 632 | 45,914 | 47,521 | 13,000 |  |  |  | 0 | 0
Commercial Solar PV | 6 | 30 | 861 | 62,550 | 64,740 | 10,000 |  |  |  | 0 | 0
Residential Solar PV | 6 | 30 | 1,119 | 81,294 | 84,139 | 14,000 |  |  |  | 0 | 0
Onshore Wind | 6 | 30 | 924 | 67,128 | 69,365 | 23,000 | 0.05306 | 0 | 0.005306 | 0 | 0
Fixed Offshore Wind | 6 | 30 | 2,314 | 168,110 | 196,268 | 71,000 |  |  |  | 0 | 0
Floating Offshore Wind | 6 | 30 | 3,743 | 271,925 | 317,472 | 61,000 |  |  |  | 0 | 0
Li-ion Battery | 6 | 30 | 250 | 18,162 | 18,707 | 6,395 |  |  |  | 0 | 0
Pumped Hydro Storage |  |  | n/a | n/a | n/a | 18,700 |  |  |  | 0 | 0
Run-of-River Hydro |  |  | n/a | n/a | n/a | 47,000 |  |  |  | 0 | 0
Reservoir Hydro |  |  | n/a | n/a | n/a | 18,700 |  |  |  | 0 | 0
Fusion | 6 | 40 | 8,500 | 564,923 | 631,584 | 84,738 |  | 10.54 | 0 | 9.34 | 11.34
Fusion fuel cost is from vacuum vessel degradation.
This value assumes 100% capacity factor

## Slide 3
Model Details: Summary
Resource | Resource Class | Annual availability (%)
Onshore Wind | 7 | 36.0
Fixed Offshore Wind | 1 | 51.1
Floating Offshore Wind | 11 | 51.1
Resource | Resource Class | Annual availability (%)
Utility-scale Solar PV | 9 | 16.8
Commercial Solar PV | 9 | 9.6
Residential Solar PV | 9 | 8.9
Resource | Charging Efficiency (%) | Discharge Efficiency (%) | Round-Trip Efficiency (%)
Li-ion Battery | 92 | 92 | 85
12-hour Pumped Hydro Storage | 90 | 90 | 81
We assumed the Li-ion batteries can have any power – energy ratio, it’s not limited to 4-hours / 6-hours, etc

## Slide 4
Model Details: Summary
We assumed no more run of river hydro or pumped hydro storage could be built, but that there was:
1960.5 MWe of pre-existing r-o-r hydro
1798 MWe of pumped hydro storage (21576MWhe of storage)
Resource | Utility-scale Solar PV | Commercial Solar PV | Residential Solar PV | Onshore Wind | Fixed Offshore Wind | Floating Offshore Wind | Run-of-River Hydro | Pumped Hydro Storage
Maximum new installed capacity (GWe) | 22 | 12 | 6 | 10 | 37.5 | 275 | 1.9605 | 1.798
Minimum new installed capacity (GWe) | 0 | 0 | 0 | 0 | 1.608 | 7.312 | 0 | 0
Pre-existing installed capacity (GWe) | 0 | 0 | 0 | 0 | 0 | 0 | 1.9605 | 1.798
Maximum allowed installed capacity for certain resources, across all ISO-NE