## Slide 1
Sesame – GenX comparison, Vol. II
Ruaridh Macdonald, Amanda Farnsworth
Version: 15th August, 2023

## Slide 2
Comparison Overview
We built a simplified model of ISO-NE which could be modelled by both Sesame and GenX, given the features and resources which can be modelled in both.
  Both models were fully linearized, removing ramping constraints, minimum powers, etc.
Sesame and GenX were compared based on:
  The total system cost: investment costs, fixed O&M, variable O&M, and fuel costs
  Installed capacity of each generator
  Capacity factor of each generator
Last week:
  We found Sesame and GenX gave very different answers, which could not be explained by solver tolerances
  Both systems gave very different total system costs, even when forced to install the same number of FPPs
This week:
We found that Sesame and GenX were processing the input costs differently, resulting in different annualized costs
Once this was resolved, both models produce the exact same results when using the same fusion power plant model
  The full fusion model in GenX leads to different results

## Slide 3
Model Details
Resource | Annualized Capital Cost ($/kWe) | Fixed OM Cost ($/MWe/yr) | Variable OM Cost ($/MWh-e) | Fuel Cost ($/MWh-e)
Natural Gas CombCycle | 33,300 | 28,000 | 2 | 44.6
Nat Gas CombCycle + CCS | 62,800 | 60,000 | 6 | 56.2
Utility-scale Solar PV | 27,700 | 13,000 |  | 
Onshore Wind | 38,900 | 38,900 |  | 
4hr Li-ion | 52,100 | 17,000 |  | 
Fixed Offshore Wind | 129,900 | 71,000 |  | 
Fusion | 521,200 | 146,000 | 3.0 | 0
Generation and storage resources allowed in each zone
Resource | Utility-scale Solar PV | Onshore Wind
Maximum installed capacity (GWe) | 22 | 10
Maximum allowed installed capacity for certain resources, across all ISO-NE
QC
ISO-NE
Demand metric (MWe) | Mean | Median | Max | Min
ISO-NE | 21719 | 21867 | 42825 | 9912
Descriptions of annual electricity demand in the model (MWe)

## Slide 4
Model Details
Sesame and GenX have different representations of fusion power plants
Sesame model and GenX-Simple
Fusion reactor treated as a typical thermal generator
$ 8,500/kWe total capital cost
All vacuum vessel costs are treated as upfront capital costs
  Not clear if this is one or all required vacuum vessels
GenX-Variable Cost
Vacuum vessel moved to variable costs
  This ensures all required vacuum vessels are included
GenX – Full model
Vacuum vessel replacement modelled explicitly
Fuel modelled explicitly

## Slide 5
Results: Summary
Total system cost comparison
 | Sesame | GenX Simple Fusion | GenX Variable VV | GenX Full Fusion
Total | $ 73.50 | $ 73.51 | $ 75.65 | $ 75.99
Cap + FOM | $ 68.10 | $ 68.10 | $ 68.34 | $ 71.02
Capacity | $ 48.30 |  |  | 
FOM | $ 19.80 |  |  | 
VOM + Fuel | $ 5.40 | $ 5.41 | $ 7.32 | $ 4.97
VOM | $ 1.50 |  |  | 
Fuel | $ 3.90 |  |  | 
Sesame and GenX return the same results (within solver tolerances) when both use the same model of fusion power plants
However, using the other models of fusion power plants leads to differences
  How are the second and later vacuum vessels accounted for in the simple model?
System Installed Capacity
 | Sesame | GenX Simple Fusion | GenX Variable VV | GenX Full Fusion
Solar | 22,000 | 22,000 | 22,000 | 22,000
Onshore | 10,000 | 10,000 | 10,000 | 10,000
Offshore | 10,300 | 10,000 | 16,100 | 20,500
Fusion | 10,000 | 10,200 | 7,960 | 6,000
NGCC | 1,600 | 1,600 | 1,300 | 100
NGCC+CCS | 10,000 | 10,000 | 10,600 | 11,800
4hr Li-ion | 18,200 | 17,900 | 18,300 | 20,000
Resource Capacity Factors
 | Sesame | GenX Simple Fusion | GenX Variable VV | GenX Full Fusion
Solar |  | 18.2% | 18.1% | 17.9%
Onshore |  | 34.7% | 34.4% | 33.5%
Offshore |  | 49.1% | 48.7% | 48.2%
Fusion | 79% | 80.0% | 66.1% | 57.7%
NGCC | 1% | 0.6% | 0.5% | 0.4%
NGCC+CCS | 15% | 14.9% | 14.2% | 13.3%
4hr Li-ion | n/a | n/a | n/a | n/a

## Slide 6
Fusion Power Plant Dispatch by each model, Winter
Fusion Power Plant Dispatch by each model, Summer